ESP_USB

USB-UART Bridge

RGB LED – on GPIO 48 (V1.0) or GPIO 38 (V1.1)

DEVICE:
WiFi, Bluetooth
Single Precision FPU
32 bit multiplier and Divider
JTAG for debugging
Adds 128-bit vector operations
Two ULP (Ultra low-power Processor) – one RISC, one Finite State Machine (NOT simultaneously)

PERIPHERALS:
3 UARTS:
UART0, Direct to GPIO43 and GPIO44 via IO MUX. Any pin via GPIO Mux.
U0RTS and U0CTS on pins GPIO15-GPIO16 via IO MUX. Any pin GPIO
UART1, U1TXD and U1RXD pins GPIO19/GPIO20 via IOMux. AND USB D+/D-
UART2. Not assigned.

I2C: not assigned.

SPI: 4 interfaces
SPI0: GFMA controller of-packageflash/PSRAM
SPI1: GFMA controller of-packageflash/PSRAM
SPI2: General purpose
SPI3: General Purpose

USB 2.0 OTG full-speed interface

USB Serial/JTAG controller (Internal PHY)