All input fields identified by (Node,Device,index) triplets. If the index is omitted, the record only has one value.

The motor enable Left and Right - The LEFT and RIGHT are buttons that send a command. When pressed, should ‘flash’ and send a command. The displayed status is updated based on data from the remote node - Red if disabled, green if enabled.
Command: Device 1 (left ) Device 05 (right)
Sends command ‘01|dd|ENAB’ or ‘01|dd|DISA’

Motor enable LED – This displays the current status of the motor driver, as reported by the TwoWheel device

PID mode switch : left and right - either AUTO or MANUAL. When pressed, should ‘flash’ and send a command.
Command: Device 2 (left) 6 (right)
Sends command: ‘01|dd|1’ (auto) or ‘01|dd|0’ (manual)
PID mode led: Left and right – shows state of PID – either ‘auto’ or ‘manual’
Data: Device 1 (left) Device 5 (right)
(0, dd,2) parameter is 0(disabled) or 1(enabled)

PID Auto LED: shows state of PID as reported by TwoWheeler.
Device 2 (left) and 6 (right)
(0,dd,1) – value is 0 (manual) 1 (auto)

Reboot button: Causes the remote node to reboot.
- TwoWheeler send command ‘01|01|RSET’
- JoyStick send command ‘02|01|RSET’

Battery Status: Shows the overall state of the battery.
Data: (1, 9) (Battery voltage).
Graph Range should be 10...13.
Background color indicates status
- Green (Above 12.24 volts),
- Yellow (below 12.24 down to 11.96),
- Red ( 11.96 down to 9 ).
- White (i.e. disconnected) if below 9 volts).

Joystick Enabled LED: Shows wether or not the Joystick is enabled.
Data: (2,0) (will be ‘0’ (disabled) or ‘1’ (enabled) )

PID Value Settings: Set the values of the PID device. Values are floating point.
Data: (device 2 – left, device 6- right)
P 01|dd|SETP|<value>
I 01|dd|SETI|<value>
D 01|dd|SETD|<value>
Scan Rate: 01|dd|STIM|<value> (value in millisecs)
Report Rate: 01|dd|SRAT|<value> (value in reports/hour)

Speed Slider:
The slider is a little different – if the Joystick is enabled, each represents the current value published by the Joystick. If the joystick is disabled, then these are adjustable and control the speed of each motor. In either case, the range is -100...0...100.

Set Speed: (device 3 -left device 7- right)
Command to Set: ‘01|dd|MSPD|<speed>’ (Speed is 0..+/- 100)

Read Speed: (From Joystick when joystick is enabled]
Use (2,3,2) (left) (2,3,3) (right) (value will be 0… +- 100)

GRAPH: This shows the performance of the PID device.
Use (device 2 – left, 6 – right) :
Target speed – use (1,dd,2) // dd is 1 (left) 5 (right) [setpoint]
Actual Speed – use (1,dd,3) // dd is 0 (left) 4 (right) [actual]
Commanded Speed – use (1,dd,4) // ( dd is 0(left) 4(right) [output]