## Two-Wheeler DEVICE NUMBERS (NODE 1)
Device description	LEFT	RIGHT
QUAD	00	04
LN298	01	05
PID	02	06
MOTOR	03	07
DRIVER	08 (combined)

	VOLTS	CURRENT(amps)
Battery	09	12
5Volt	10	13
Motor	11	14
INA3221 Control	15 (both

## DEVICE: 15 (Power)
Command	Description
STIM	Set time Per Sample. See INA3221 docs
SAVG	Set Averaging mode. See INA3221 docs
RATE	Set time between sames. See INA3221 docs

OUTPUT: IA3221: readCount, volt(1), Volt(2), Volt(3), I(1)ma, Ima(2), Ima(3)

## DEVICES 9 thru 14: (Sub devices of power device)
   (See Device numbers table above for assignments)

   Output: "%f" (the value for this sub device – either volts or milliamps)

## DEVICE 8: (Driver)
Command	Description
TANK <left-speed> <right-speed>	Set the left and right ‘tread’ speed
MOVE <speed> <rotation-rate	Set the speed and rotation
SPED <speed>	Set the speed (from joystick)
ROTA <rotRate>	Set the rotation (turn) rate
DRFT	Disable motor drivers, let us drift
STOP	Stop all motion

Output Data: (none)

## Device 3(left) and 7(right): MOTOR device
Commands:
   MSPD <speed> Set the speed of the motor
Output Data: (none)

## Device 2(left), 6(right) - LPID and RPID

PID device: This reads both the ln298 (current power level) and the QuadEncoder (actual speed)

Command	Description
SPID <kp>|<ki>|<kd>	Set the P, I and D coeficients
SETP <kp>	Set the K parameter
SETI <Ki>	Set the I parameter
SETD <Kd>	Set the D parameter
SMOD <0-Manual, 1-Automatic>	Set the mode of the PID device (Auto/Manual)
STIM <time>	Set sample time (milliseconds)

Output:
 “<mode>,<setPoint>,<actual>,<output>"

## DEVICE 0 (left Quad) 4(right Quad) Quadrature encoders
Commands:

Command	Description
QSET <pulsesPerRev> <circumnfrence>	Set the wheel parameters. Circum in mm
QSCK <updateRate>	Set how often we update speed
QRST	Reset current position to 0.

Output: <position>,last_speed, name

= = = = = = = = = = =
## ln298 device ( left 1, right 5) –
Comand	Description
SPWM <pulseWidth>	Set the pulse width ( 0… +/-100)
ENAB	Enable the driver
DISA	Disable the driver

Output:
   pulse-width,"DIS"/"ENA"