## Two-Wheeler DEVICE NUMBERS (NODE 1)
Device description	LEFT	RIGHT
QUAD	00	04
LN298	01	05
PID	02	06
MOTOR	03	07
DRIVER	08 (combined)

	VOLTS	CURRENT(amps)
Battery	09	12
5Volt	10	13
Motor	11	14
INA3221 Control	15 (both

## Start up and enable motors:
01|02|SMOD|F (disable left PID)
01|06|SMOD|F (disable right PID)
01|01|ENAB (Enable left motor)
01|05|ENAB (Enable right motor)
## INA3221 device:
   Commands:
      STIM <timeInMsec> Set Time per sample. See INA3221 docs
      SAVG <cpde> Set Averaging mode. See INA3221 docs
      RATE <timeInMs> Set time between samples (Sample Rate) in (ms). Max is 32765

   Data format:
      IA3221: INAX|%llu|%f|%f|%f|%f|%f|%f",tmpCount, volt(1), Volt(2), Volt(3), Ima(1), I(2), I(3)

SUBDEVICES:
   Volt0, Volt1, Volt2, Current0, Current1, Current2

   Output:
     "%f" (the value for this subdevice)

## DRIVER device

Commands(8)
   TANK <left-speed> <right-speed> ;
   MOVE <speed> <rotRate> ; set for given speed/rotation rate
   SPED <speed> (from joystick) ; set the speed
   ROTA <rotRate> (from joystick) ; set the rotation rate
   STOP ; stop all motion
   DRFT ; disable drivers, drift...

Output Data:

## MOTOR device
Commands:
   MSPD <speed> ; Set motor speed - 0 +/- 2047.

Output:

## PID controls

PID device: This reads both the ln298 (current power level) and the QuadEncoder (actual speed)

Commands for the PID device (left 2, right 6)
   // SPID <kp> <ki> <ki> ; Set the P.I.D. coeficients
TANK <e-val>|<l-val> ; Set the target speed (0... +/- 100)
      resp: "EROR, Wrong number of arguments in SPED command"
      resp: "OK,<val>

   SETP <val>
      resp: "EROR,Wrong number of arguments in SETP command");
      resp: OK,<val>

   SETI <val>
      resp: "EROR,Wrong number of arguments in SETI command");
      resp: OK,<val>

   SETD <val>
      resp: "EROR,Wrong number of arguments in SETD command");
      resp: OK,<val>

   SMOD <bool> ; PID controler mode: true=automatic, false=manual.
      resp:SMOD,<bool> ; bool 1 == Automatic or 0==manual
      resp: EROR,Wrong number of arguments

   STIM <time> ; set sample time (millisecs)
      resp:EROR,Wrong number of arguments
      resp:STIM,<time>

Output:
 "<02/08>|<setPoint>,<actual>,<output>"

   "EROR,pid - unknown command"

## QUADRATURE encoder
Commands:

   QSET <pulsesPerRev> <circum_mm> ; Set parameters for quadrature decoder.
      "EROR,Pulse Count must be >0"
      "EROR, Wheel diam must be >0"
      "EROR, Wrong number of arguments"
      "QSET,<wheelDiam>,<pulsePerRev>,pulsesToDist"

   QSCK <updateRate> ; Set how often we update the speed (in millisecs)
      "EROR,wrong number of arguments"
      "OK,SCLK,<spdCheckRate>

   QRST ; reset position to '0.0'

Output:
   <position>,last_speed, name

= = = = = = = = = = =
## ln298 device ( left 1, right 5)
    SPWM <pulseDidth> ; set the pulse width for this motor (0...+/- 100)
      "ERR,Wrong number of arguments in SPED command");
      resp: 'OK|SPWM|Pulse width is <val>
    ENAB ; Enable the Driver
      resp: "OK|ENAB|<name> enabled"
    DISA ; Disable the Driver
      resp: "OK|DISA|<name> disabled"

    resp: "EROR|LN298|Unknown command"

Output:
   duty-cycle,"DIS"/"ENA"

## ADITIONAL SMAC MESSAGES
 (In all cases, '%s' will idenify the specific parameter).
 ( '%d' is the index of the word - the original command is '0').
   "EROR,%s,Missing argument no %d"
   "EROR,%s,argument %d is not an unsigned int"
   "EROR,%s,Missing argument no %d
   "EROR,%s,Argument %d is not a int"
   "EROR,%s,Invalid double for argument no %d",
   "EROR,%s,Unknown boolean value for argument %d"